## Slide 1: National Forest Monitoring Systems

## Slide 2
By the end of this module, you should be able to:
Define a National Forest Monitoring System;
Describe the process and functions of developing a National Forest Monitoring System;
Identify tools available in developing a National Forestry Monitoring System;
Describe the Measurement, Reporting and Verification process for REDD+.

## Slide 3
Measurement is concerned mostly with the estimation of Ads and EFs
Reporting to the UNFCCC on progress with REDD+ through NC and BURs (Biennial Update Reports)
Verification is done by Independent Experts (3rd Party) contained in UNFCCC Roster
Activity data: data on magnitude of human activity resulting in emissions during a given period of time
Emission factor: coefficient that relates activity data to the amount of GHGs released
Removal factor: rate at which carbon is taken up from the atmosphere by a terrestrial system and sequestered in biomass and soil
Tier: source of data used in calculation of emissions when reporting
IPCC Land Representation: Six land use categories (Forest Land, Crop land, Grassland, wetland, settlement, Other Land)
Key terminology
National Forest Monitoring Systems

## Slide 4
What is an NFMS?
National Forest Monitoring Systems
System for measuring and monitoring how land is used in a country and for estimating forest-related GHG emissions and removals
Ultimate aim is to make reliable GHG emission estimates
Composed of two functions: the MRV (Measurement, Reporting & Verification) function and the Monitoring function

## Slide 5
The MRV function is supported by 3 technical “pillars “ or building blocks:
Satellite Land Monitoring System (SLMS) for collection and assessment of data on land use/land use change (Activity Data)
P2: National Inventory (NFI) for collection of information on forest carbon stocks and stock changes, needed to estimate emission factors
P3: A National GHG Inventory used as tool for reporting anthropogenic forest-related GHG emissions by sources and removals by sinks to the UNFCCC Secretariat
The MRV Function
National Forest Monitoring Systems

## Slide 6
Assessment Area Change: Activity Data & Approaches
National Forest Monitoring Systems

## Slide 7
REDD+ MRV: Emission Factors (EF)
National Forest Monitoring Systems
The “Tiers” system represent different levels of methodological complexities, and vary from Tiers 1 to Tiers 3.
  Tier 1 is basic and is used as s default EF data, provided by IPCC Guidelines & Guidance, and can also be obtained from the Emissions factor Database (EMFDB). It is appropriate for countries where national data is scarce or absent and hence default values have to be used.
  Tier 2 is intermediate but uses EFs that are country- or region-specific for the most important or “Key Carbon Pools”.
  Tier 3 uses higher order methods , including models and inventory measurement systems tailored to address national circumstances.
  Tier 2 & 3 are sometimes referred to as higher order tier methods and provide more accurate estimates of greater certainty than Tier 1.

## Slide 8
With the full development and operation of the two elements (AD and EF) of the MRV system a country can generate its REDD+ related National GHG‐I, for reporting to the UNFCCC (in Phase III of REDD+).
The National GHG‐I for REDD+ is incorporated into the National GHG‐I, which will be submitted every four years as its National Communication (NC) to UNFCCC.
Under Articles 4 and 12 of the UNFCCC, all Parties are required to prepare NCs.
Information reported in GHG‐I represents an essential link between science and policy, and provides the means by which the Conference of Parties (COP) can monitor progress made by Parties in meeting their commitments and in achieving the Convention's ultimate objectives
REDD+ MRV: GHG‐Inventory
National Forest Monitoring Systems

## Slide 9
Monitoring function intends to assess REDD+ performance throughout its 3 phases (e.g Performance of REDD+ Demonstration Activities in Phase 2 & REDD+ PAMs in Phase 3)
In addition to Remote Sensing, ground-based monitoring approaches can be utilized, including community monitoring.
The Monitoring Function & REDD+ Phases
National Forest Monitoring Systems

## Slide 10
Satellite Remote Sensing | Cost-effective method to monitor deforestation and to some extent degradation?
Web-based Portals | Transparent means to monitor outcomes of PAMs implementation, allows users to provide feedbacks and user-interactions
Community monitoring | Bottom-up means to incorporate local knowledge into monitoring. Means to ensure effective engagement of IPs in monitoring & Reporting
Other forest monitoring systems | Builds linkages with existing monitoring systems
Monitoring Tools
National Forest Monitoring Systems

## Slide 11
Summary of Important COP decisions
National Forest Monitoring Systems
Agreement |  | Summary
The UNFCCC: Text of the Convention (1992), Article 4: Commitments: | 1992 | Parties will publish and make available national inventories of anthropogenic sources and removals by sinks, using similar methods.
The Bali Action Plan (2007) | 2007 | All parties are encouraged to reduce their GHG emissions in ways that are Measurable, Reportable and Verifiable (MRV) Capacity building should be supported and reporting using the latest IPCC guidelines encouraged.
Copenhagen (2009) | 2009 | Emissions from forests should be reduced according to the latest IPCC guidelines and national forest monitoring systems should be established according to using consistent methodologies.
Cancun (2010) | 2010 | A National forest monitoring system is one of the four key elements of REDD+ and it should be developed through a phased approach.
Warsaw (2013) | 2013 | Formalises earlier guidance into decisions, describes the quality of national forest monitoring systems required for measurement of REDD+ results, and the methods of reporting and verification.

## Slide 12
IPCC Methodological Guidance are useful in the implementation of NFMS:
    Revised 1996 IPCC Guidelines
    Good Practice Guidance (GPG) 2000
    GPG 2003 (LULUCF)
    2006 IPCC Guidelines
Using Software Tools to support the Guidelines (e.x. Emission Factor Database: EFDB)
IPCC Guidelines/Guidance help to demonstrate the Good Practices to be used by all countries in reporting to UNFCCC (TACCC: Transparency, Accuracy, Consistency, Completeness & Comparability).
Implementing NFMS: IPCC Guidelines
National Forest Monitoring Systems
TACCC

## Slide 13
Measuring forest carbon stock changes
National Forest Monitoring Systems
Stock difference & Gain-Loss Methods

## Slide 14
Measurement, Reporting and Verification (MRV) for REDD+
National Forest Monitoring Systems

## Slide 15
Main components of a NFMS for REDD+ include the satellite Land Monitoring System and the National Forest Inventory
Key principles of IPCC’s guidance for MRV for REDD+ are: TACCC: Transparent, Documented, consistent over time, Complete, Comparable, assessed for Uncertainty
MRV for REDD+ involves
  Measurement: AD x EF=Emissions
  Reporting through NC and BUR on GHG Emissions
  Verification through 3rd Party (external) Reviewers
TACCC